## Slide 1: Automatic Pipe Cutting Machine
Group No :39
IN 1900 ( ICT Project)
Final Evaluation

## Slide 2: Group Members
 | Name | Reg. No: | Photo
Group Leader | D.S. Rathnasinghe | 204178K | 
Member 1 | P.K.D.P. Chathurangi | 204027A | 
Member 2 | P.H.A.E. Madhubhashini | 204117B | 
Member 3 | J.D.A. Shalinda | 204200A | 
Member 4 | K.M. Tharangana | 204215A | 

## Slide 3: Outline
Problem In Brief
Project Aim And Objectives
Proposed Solution – 3D Model, Block Diagram
Schematic Diagram Of The System
PCB Design
Resource Required
Cost Estimation
Test And Implementation
Individual Contribution

## Slide 4: Problem in Brief
If we consider existing manual and semi automatic machines that are used to cut pipes in the industry, we can identify following issues .
Time-consuming is high
Need more human intervention
Most of the time one machine is limited to cut one material.
The level of safety is low

## Slide 5: Project Aim & Objectives
Aim:
Design and develop a fully automated pipe cutting machine
to measure and cut PVC pipes, steel pipes and box bars.
Objectives:
To measure and cut pipes automatically
To cut pipes of different materials
To reduce manpower
To increase the safety level of the operator

## Slide 6
Proposed Solution (3D Model)

## Slide 8: Proposed Solution (Cont’d)
Distance to pipe (left)
2. Distance to pipe (Right)
3. Distance to clutch 1
Display commands
Turn on DC motors
Turn on stepper motors
Presence of pipe
Material of Pipe
Inductive Proximity sensor
1. Length
2.Quantity
IR sensors
Inputs
Outputs
Ultrasonic sensors
LCD Display
Microcontroller
Keypad
Stepper Motors
Move Clutch 1, Clutch 2 and Clutch 3.
Control the Cutting Arm
  DC Motors
Rotate the Screw Rod
Rotate the Cutting Blade

## Slide 9
Schematic Diagram of the System

## Slide 10
Schematic Diagram of the System (Cont’d)

## Slide 11
PCB Design

## Slide 12: Resource Required
Software:
  Atmel Studio
  Blender
  Proteus
  Hardware:
  Sensors: IR Sensor, Ultrasonic Sensor, Inductive Proximity Sensor
  Microcontroller: Atmega32
  Keypad
  Motors : DC Motor , Stepper Motors
  Drivers : DC Motor(L1293), Stepper Motor(ULN 2003)
  Grinding Disc
  LCD
  Power Supply Unit

## Slide 13
Click to add text
Components | Units | Unit Price | Price
Microcontroller | 2 | Rs: 550.00 | Rs: 1100.00
IR Sensor | 3 | Rs: 120.00 | Rs: 360.00
Inductive Proximity Sensor | 1 | Rs: 550.00 | Rs: 550.00
Ultrasonic Sensor | 3 | Rs: 400.00 | Rs: 1200.00
Keypad | 1 | Rs: 160.00 | Rs: 160.00
LCD | 1 | Rs: 800.00 | Rs: 800.00
Stepper Motor | 4 | Rs: 3200.00 | Rs:12800.00
DC Motor | 3 | Rs: 950.00 | Rs: 2850.00
Grinding Disc | 1 | Rs: 2000.00 | Rs: 2000.00
Drivers ULN2003 (Stepper motors) | 4 | Rs: 460.00 | Rs: 1840.00
Drivers L1293 (DC motor) | 3 | Rs: 400.00 | Rs: 1200.00
Other expenses |  |  | Rs: 5000.00
Total |  |  | Rs: 29860.00
Cost Estimation

## Slide 14: Test and Implementation
The process of this machine can be tested under the following sub-processes.
1.Entering user inputs 2.Detecting the pipe and Identifying the material
3.Tightening process
4.Aligning process
5.Measuring process
6.Cutting process
7.Wastage Separating and Collecting process

## Slide 15: 1. Entering user inputs
At the beginning user must enter the needed length and quantity of the pipe through keypad.
LCD is guiding user to enter them.

## Slide 16: 2.Detecting the pipe and Identifying the material
To start the process, the operator must switch on the machine and place the pipe between clutches.
Then the machine will detect the presence of the pipe by the IR sensor and will identify the material of the pipe by the Inductive proximity sensor .
 | Positive signal (1) | Negative signal (0)
Positive signal (1) | Metal pipe detected | No object .Machine will not start.
Negative signal (0) | Non-metal (PVC) pipe detected | 
IR
I.P.S

## Slide 17
By using the results of the process 1 , machine will decide the following things.
1. Speed of the cutting blade
2. Relevant bin (side) for the wastage
After that , Tightening process will start.

## Slide 18: 3.Tightening Process
After detecting and identifying the pipe, clutches will automatically move in and the pipe will be tightened.
There are four clutches which are used in the tightening process.
Two Ultra-sonic sensors are placed in both 1&2 clutches to identify the distance to the pipe by each side.

## Slide 19: Technique for Tightening Process
Inside look of the clutch
Screw Rod

## Slide 20: Calculations
Relationship between Moving distance of the clutch and Step angle of the Stepper Motor :
Step angle of the stepper motor = 1.8
Number of steps rotated within a cycle = 360 /1.8 =200
Clutch moving distance for a step = Pitch of the screw rod /200
We can get the pitch of the relevant screw rod by using a graph.

## Slide 21: 4. Aligning Process
Two IR sensors will be used for this process.
Clutches will move the pipe forward and backward on the rails until aligning to the correct position .
Not aligned
Not aligned Aligned
(Correct position)

## Slide 22: Technique for Moving Clutch (Rail System)
Screw Rod

## Slide 23: 5.Measuring Process
At the beginning, the operator must enter the needed length and quantity through the keypad.
Ultra-sonic sensor will be used to measure the length of the pipe.
The pipe will be moved forward by the clutches which are connected to the rail system.

## Slide 24: 6.Cutting Process
Here the cutting arm, which is controlled by the stepper motor, will come down and cutting blade will start rotating and cutting the pipe according to the pre-decided speed.

## Slide 25: 7. Wastage Separating and Collecting Process
At the end of the cutting process, the remaining piece of pipe will be kept between clutch 3 and clutch 4.
If the length of this piece is less than 10cm, the machine will consider it as a wastage.
IR sensor will be used to identify this.

## Slide 26: Technique for Separating Process
If the remaining piece is identified as a waste, it will be grabbed by clutch 1 and clutch 2 and will be released to the relevant bin.
There are two bins placed inside the machine for this purpose.
Separating plastic wastage
Separating metal wastage

## Slide 27: Test and Implementation
Individual Contribution

## Slide 28
Responsibilities:
Stepper Motor
Ultrasonic Sensor
Member 1– P.K.D.P.Chathurangi (204027A)

## Slide 29
01.Stepper Motor
Datasheet:
https://www.omc-stepperonline.com/nema-17-stepper-motor-datasheet/nema-17-unipolar-1-8deg-15-8ncm-22-4oz-in-0-31a-12v-42x42x33mm-6-wires.html

## Slide 30
Internal structure:
Specifications:
Maximum current: 1.5A-1.7A
Maximum voltage: 12 VDC
Step Angle : 1.8 degree
Unipolar
200 Steps per revolution, 1.8 degrees
No. of Phases: 4
Model- Nema 17

## Slide 31
Working Principle
A
B
C
D
B
A
C
D

## Slide 33
Code for Stepper Motor
#define F_CPU 16000000UL
#include "stepper.h"
int main(void)
{
initSteppers();
rotateStepper_1(1,4);
}
#include "stepper.h"
void initSteppers(){
DDRA = 0xFF;
DDRC = 0xFF;
}
void rotateStepper_1(int direction, float distance)
{
// clockwise-1
// Counterclockwise-0
// 1 distance unit = 1 rotating
int period;
period = 100;
if (direction == 1)
{
for (int i = 0; i < round(distance); i++)
{
PORTA = 0x03;
_delay_ms(period);
PORTA = 0x06;
_delay_ms(period);
PORTA = 0x0c;
_delay_ms(period);
PORTA = 0x09;
_delay_ms(period);
PORTA = 0x03;
_delay_ms(period);
}
}
else
{
for (int i = 0; i < round(distance); i++)
{
PORTA = 0x03;
_delay_ms(period);
PORTA = 0x09;
_delay_ms(period);
PORTA = 0x0c;
_delay_ms(period);
PORTA = 0x06;
_delay_ms(period);
PORTA = 0x03;
_delay_ms(period);
}
}
}
// header files
#ifndef STEPPER_H_
#define STEPPER_H_
#define F_CPU 16000000UL
#include <avr/io.h>
#include <util/delay.h>
void initSteppers();
void rotateStepper_1(int direction, float distance);
#endif /* STEPPER_H_ */

## Slide 34
Specifications
Maximum current-15mA
Maximum Voltage- 5V
Range-2cm-400cm
Measuring angle: 15 degree
Trigger input pulse: 10 micro-seconds
02.Ultasonic Sensor
Datasheet:https://www.mouser.in/datasheet/2/813/HCSR04-2307007.pdf

## Slide 35
Initial stage
After tightening process

## Slide 36
Working principle
Time which echo pin remain high is captured.

## Slide 39
Speed = distance/ time​
​
Distance= speed x time​
​
(speed of sound wave is 343 meters per second at standard temperature and pressure, approx.-340) ​
​
Distance to object= 340 x time /2 (since wave is going back and forth)​
= 170 x time meters​
​
1/distance = 1/ 170 x time​
1/distance =1000,000/170 x 100 x time centimeters​
1/distance =58.8/time​
​
Distance = time/58
Building the code – counting distance

## Slide 40
Code for Ultrasonic sensor :
#define F_CPU 16000000UL
#include <avr/io.h>
#include <avr/interrupt.h>
#include <util/delay.h>
#include <string.h>
#include <stdlib.h>
#include "LCD.h"
#include "ultrasonic.h"
int main(void)
{
LCD_Init();
initUltrasonic();
int16_t count_a = 0;
char show_a[16];
sei();
while(1)
{
count_a =getUltrasonic_2_Distance();
LCD_String_xy(0, 0, "Ultrasonic");
itoa(count_a,show_a,10);
LCD_String_xy(1, 0, "Distance= ");
LCD_String_xy(1, 9, show_a);
LCD_String_xy(1, 13, "cm");
_delay_ms(200);
}
}
#include "ultrasonic.h"
static volatile int ult2_count = 0; // interger to access all though the program
static volatile int i = 0;
void initUltrasonic(){
DDRB |=(1<<PB6);
_delay_ms(50);
GICR |= (1<<INT1); //enabling interupt 1
//General Interrupt Control Register
MCUCR|= (1<<ISC10); //setting interrupt triggering logic change
// MCU control Register
TCCR1A = 0;
}
int getUltrasonic_2_Distance(){
int pulse;
PORTB |= (1<<PB6);
_delay_us(20); //triggering the sensor for 15usec
PORTB &= (~(1<<PB6));
while(ult2_count==NULL);
pulse=ult2_count;
ult2_count=NULL;
return (pulse/928)+1;
}

## Slide 41
ISR(INT1_vect) //interrupt service routine when there is a change in logic level
{
if (i==1)//when logic from HIGH to LOW
{
TCCR1B=0; //disabling counter
ult2_count=TCNT1;//count memory is updated to intege
TCNT1=0;//resetting the counter memory
i=0;
}
if (i==0)//when logic change from LOW to HIGH
{
TCCR1B|=(1<<CS10);//enabling counter
i=1;
}
}
//Header files
#ifndef ULTRASONIC_H_
#define ULTRASONIC_H_
#define F_CPU 16000000UL
#include <avr/io.h>
#include <avr/interrupt.h>
#include <util/delay.h>
#include <stdlib.h>
void initUltrasonic();
int getUltrasonic_2_Distance();
#endif /* ULTRASONIC_H_ */

## Slide 42
PCB Design for all responsible components:

## Slide 43
Member 2 - P.H.A.E.Madhubhashini (204117B)
Responsible Components :
4 x 4 Keypad
IR Sensor
Power Supply Unit

## Slide 44
1). 4 x 4 Keypad (#27899)
Usage: To get inputs from the user
1.Required length
2.Required quantity

## Slide 45
Specifications:
Maximum current: 30 mA
Maximum voltage: 24 VDC
Operating Temperature : 0 – 50 oC
Interface : 8 pin access to 4 x 4 matrix
Datasheet:https://drive.google.com/file/d/1HSuMoYTHTb9IgbnWdi8wxe0oAgE0s5xc/view?usp=sharing

## Slide 46
Internal Circuit

## Slide 47
Schematic Diagram :

## Slide 48
Keypad.h
unsigned char keypad()
{
PORTA=0b11111110;
if((PINA &(1<<PINA4))==0)
{
_delay_ms(3);
return '7';
}
else if((PINA & (1<<PINA5))==0)
{
_delay_ms(3);
return '8';
}
else if((PINA & (1<<PINA6))==0)
{
_delay_ms(3);
return '9';
}
else if((PINA & (1<<PINA7))==0)
{
_delay_ms(3);
return '/';
}
PORTA=0b11111101;
if((PINA &(1<<PINA4))==0)
{
_delay_ms(3);
return '4';
}
else if((PINA & (1<<PINA5))==0)
{
_delay_ms(3);
return '5';
}
else if((PINA & (1<<PINA6))==0)
{
_delay_ms(3);
return '6';
}
Code for Keypad :
Keypad.c
else if((PINA & (1<<PINA7))==0)
{
_delay_ms(3);
return '*';
}
PORTA=0b11111011;
if((PINA &(1<<PINA4))==0)
{
_delay_ms(3);
return '1';
}
else if((PINA & (1<<PINA5))==0)
{
_delay_ms(3);
return '2';
}
else if((PINA & (1<<PINA6))==0)
{
_delay_ms(3);
return '3';
}
else if((PINA & (1<<PINA7))==0)
{
_delay_ms(3);
return '-';
}

## Slide 49
PORTA=0b11110111;
if((PINA &(1<<PINA4))==0)
{
_delay_ms(3);
return 'C';
}
else if((PINA & (1<<PINA5))==0)
{
_delay_ms(3);
return '0';
}
else if((PINA & (1<<PINA6))==0)
{
_delay_ms(3);
return 'E';
}
else if((PINA & (1<<PINA7))==0)
{
_delay_ms(3);
return '+';
}
}
Main.c
int main(void)
{
DDRA=0x0F;
lcd_init();
lcd_print(" HELLO USER ");
_delay_ms(100);
label1:
lcdcmd(0x01);
lcdcmd(0x0E);
delay_ms(100);
lcd_print("ENTER LENGTH");
lcdcmd(0xC0);
do
{
PORTA=0xF0;
if(PINA!=0xF0)
{
x=keypad();
if(x=='/'||x=='*'||x=='-'||x=='C')
{
lcdcmd(0x01);
lcdcmd(0x0E);
_delay_ms(100);
lcd_print("INVALID INPUT");
_delay_ms(100);
goto label1;
}
else if(x!='E')
{
x1=(x1*10)+(x-'0');
lcddata(x);
}
}
}while(x!='E');
label2:
lcdcmd(0x01);
lcdcmd(0x0E);
_delay_ms(100);
lcd_print("ENTER QUANTITY :");
_delay_ms(100);
lcdcmd(0xC0);
do
{
PORTA=0xF0;
if(PINA!=0xF0)
{
y=keypad();
if(y=='/'||y=='*'||y=='-')
{
lcdcmd(0x01);
lcdcmd(0x0E);
_delay_ms(100);
lcd_print("INVALID INPUT");
_delay_ms(100);
goto label2;
}
else if(y!='E')
{
x2=y-'0';
lcddata(y);
}
}
}while(y!='E');
if(y=='E')
{
lcdcmd(0x01);
lcdcmd(0x0E);
_delay_ms(100);
lcd_print(" Done");
_delay_ms(100);
lcdcmd(0x01);
_delay_ms(500);
}
return 0;
}

## Slide 50
2). IR Sensor
1
2
3
1 - VCC
2 - Ground
3 - Output
Usage : 1. To detect the presence of the pipe
2. To identify the wastage of the pipes

## Slide 51
Specifications:
Supply current - 20 mA
Operating voltage: 5 VDC
Range: up to 20 cm
Elements of IR sensor
Datasheet:https://drive.google.com/file/d/1d3HOpQUuzncxyCeDQ7-yZyzzkoH_pUXo/view?usp=sharing

## Slide 52
Working Principle and Internal Circuit
This internal circuit consist of IR LED and IR Photo-diode.
IR LED acts as IR transmitter and IR photo-diode acts as IR receiver.
LM 358 IC has been used as a low power dual operational amplifier in this circuit.

## Slide 53
Schematic Diagram :​

## Slide 55
PCB Design for Keypad and IR Sensor :

## Slide 56
3). Power Supply Unit
Schematic Diagram

## Slide 57
Rectification
L7805 Regulator
(5V)
After Smoothing :

## Slide 58
PCB Design

## Slide 59
Power calculation to select the suitable transformer to the power supply unit:
https://drive.google.com/file/d/1ZP28eiGIYe9E7ZHggpAdx_H_i682eJCu/view?usp=sharing

## Slide 60
Member 3- D.S. Rathnasinghe(204178K)
Responsible Components :
DC motor(Rail system)
IR sensor(Aligning process)
Other:
USART communication

## Slide 61
DC Motor
Datasheet:
https://www.handsontec.com/dataspecs/motor_fan/775-Motor.pdf

## Slide 62: Technique for Moving Clutch (Rail System)
Screw Rod

## Slide 63
Internal structure:
Specifications:
Maximum current: 1.5A
Maximum voltage: 20 VDC
Motor Type : 775
Weight : 350g
No Load Speed : 12,000 RPM @ 12V.
Stall Torque : 79Ncm @ 14.4V.
Overall Size : 98x42mm.

## Slide 64
Working Principle

## Slide 66
Code for DC Motor :
#define F_CPU 16000000UL
#include "dcmotor.h"
void initDCMotors(){
DDRB |= (1<<PB0) | (1<<PB1);
}
void rotateDCMotors(int direction)
{
  if (direction != 0){
  // Rotate DC motor Clockwise ?
    PORTB &= ~(1 << PB0);
    PORTB |= (1 << PB1);
  }
  else{
  // Else rotate DC motor Counterclockwise
    PORTB |= (1 << PB0);
    PORTB &= ~(1 << PB1);
  }
}
void stopDCMotors()
{
  // stop Rotation DC motor
  PORTB &= ~(1 << PB0);
  PORTB &= ~(1 << PB1);
}
Header File
#ifndef DCMOTOR_H_
#define DCMOTOR_H_
#define F_CPU 16000000UL
#include <avr/io.h>
void rotateDCMotors(int direction);
void stopDCMotors();
void initDCMotors();
#endif /* DCMOTOR_H_ */

## Slide 67
2. IR Sensor
Maximum current: 20 mA
Maximum voltage: 5 VDC
Datasheet:
https://drive.google.com/drive/folders/1-g542Yw-wO8iKtjyBc5C5We-NeQ-pRMK?usp=sharing
1
2
3
1 - VCC
2 - Ground
3 - Output

## Slide 68: Usage:Aligning Process
Two IR sensors will be used for this process.
Clutches will move the pipe forward and backward on the rails until aligning to the correct position .
Not aligned
Not aligned Aligned
(Correct position)

## Slide 69
Specifications:
Maximum current –20 mA
Operating voltage: 5 VDC
Range : 2cm – 30 cm
Elements of IR sensor

## Slide 70
Internal Circuit
This internal circuit consist of IR LED and IR Photo-diode.
IR LED acts as IR transmitter and IR photo-diode acts as IR receiver.
LM 358 IC has been used as a low power dual operational amplifier in this circuit.

## Slide 72
Code for IR Sensor :
#define F_CPU 16000000UL
#include <avr/io.h>
#include "dcmotor.h"
int main(void)
{
initDCMotors();
  if ((PIND & 1 << PD5) && (PIND & 1 << PD6)){
  // if both Ir sensor-2,3 are detected pipe
  rotateDCMotors(1);
  while (PIND & (1 << PD6));
  }
  else if (!(PIND & 1 << PD5) && !(PIND & 1 << PD6)){
  // else if both Ir sensor-2,3 are not detected pipe
  rotateDCMotors(0);
  while (!(PIND & (1 << PD5)));
  }
stopDCMotors();
}

## Slide 73
USART communication
Ways to connect microcontrollers
USART (Universal Synchronous Asynchronous Receiver Transmitter)
SPI ( Serial Peripheral Interface)
I2C (Inter-Integrated Circuit)
Why USART?
Only two devices to connect
Simplicity to implement
Asynchronous
full duplex communication
Used pins of atmega 32
TxD: Transmit Data
RxD: Receive Data

## Slide 75
Code For USART :
#include "usart.h"
void initUSART(long USART_BAUDRATE){
  DDRD |= 1 << PIND1;//pin1 of portD as OUTPUT
  DDRD &= ~(1 << PIND0);//pin0 of portD as INPUT
  //Put the upper part of the baud number here (bits 8 to 11)
  UBRRH = (unsigned char) (BAUD_PRESCALE(USART_BAUDRATE) >> 8);
  //Put the remaining part of the baud number here
  UBRRL = (unsigned char) BAUD_PRESCALE(USART_BAUDRATE);
  //Enable the receiver, transmitter
  UCSRB = (1 << RXEN) | (1 << TXEN);
  //Set 2 stop bits and data bit length is 8-bit
  UCSRC = (1 << USBS) | (1 << UCSZ0) | (1<<UCSZ1);
}
uint8_t getReceivedData(){
  while ((UCSRA & (1 << RXC)) == 0);/* Wait till data is received */
  return(UDR);
}

## Slide 76
Continued..
void sendData(uint8_t byte){
  while (! (UCSRA & (1 << UDRE)) );
  {
  UDR = byte;//once transmitter is ready sent eight bit data
  }
  // Get that data out here!
  _delay_ms(5);
}
Header File :
#ifndef USART_H_
#define USART_H_
#define F_CPU 16000000UL
#define BAUD_PRESCALE(USART_BAUDRATE) (((F_CPU / (USART_BAUDRATE * 16UL))) - 1)
#include <avr/io.h>
#include <util/delay.h>
void initUSART(long USART_BAUDRATE);
void sendData(uint8_t byte);
uint8_t getReceivedData();
#endif /* USART_H_ */

## Slide 77
PCB Design for all responsible components:

## Slide 78
Member 4- J.D.A. Shalinda (204200A)
Responsible Components :
Stepper Motor (For cutting arm)
DC Motor (For cutting blade)
Inductive Proximity Sensor

## Slide 79
1. Stepper Motor ( For the Cutting Arm)
Datasheet:
https://components101.com/sites/default/files/component_datasheet/NEMA17.pdf
https://components101.com/motors/nema17-stepper-motor

## Slide 80
Internal structure:
Specifications:
Maximum current range: 1.5A-1.7A
Maximum voltage: 12 VDC
Step Angle : 1.8 degree
Unipolar
200 Steps per revolution, 1.8 degrees
Holding torque of 3.2 kg-cm (0.32Nm)
Model : NEMA 17

## Slide 81
Working Principle
A
B
C
D
A
D
C
B

## Slide 83
Code for Stepper Motor :
#define F_CPU 16000000UL
#include <avr/io.h>
#include <util/delay.h>
void initSteppers(){
DDRC = 0xFF;
}
void rotateStepper_4(int direction){
// clockwise-1
// Counterclockwise-0
int period;
period = 100;
if (direction == 1)
{
/* Rotate clockwise */
PORTC = 0x30;
_delay_ms(period);
PORTC = 0x60;
_delay_ms(period);
}
else
{
/* Rotate Counterclockwise */
PORTC = 0x60;
_delay_ms(period);
PORTC = 0x30;
_delay_ms(period);
}
}
int main(void)
{
initSteppers();
rotateStepper_4(1);
_delay_ms(2000);
rotateStepper_4(0);
}

## Slide 84
2. DC Motor (For the Cutting Blade)
Datasheet:
https://www.handsontec.com/dataspecs/motor_fan/775-Motor.pdf

## Slide 85
Internal structure:
Specifications:
Maximum current: 1.5A
Maximum voltage: 20 VDC
Motor Type : 775 Model
Weight : 350g.
No Load Speed : 12,000 RPM @ 12V.
Stall Torque : 79Ncm @ 14.4V.

## Slide 86
Working Principle & Application

## Slide 88
#define F_CPU 16000000UL
#include <avr/io.h>
#include <util/delay.h>
#include "dcmotor.h"
int main()
{
initDCMotor();
_delay_ms(2000);
rotateMotor();
_delay_ms(2000);
stopMotor();
_delay_ms(2000);
setMotorSpeed(10);
rotateMotor();
_delay_ms(2000);
stopMotor();
_delay_ms(2000);
}
#include "dcmotor.h"
void initDCMotor(){
DDRB |= (1 << PB3) | (1<<PB2) | (1<<PB1);
TCCR0 = (1 << WGM00) | (1 << WGM01) | (1 << COM01) | (1 << CS00);
OCR0 = 255;
}
void setMotorSpeed(int bladeMotorSpeed){
OCR0 = bladeMotorSpeed;
}
void rotateMotor(){
PORTB |=(1<<PB1);
}
void stopMotor(){
PORTB &=~(1<<PB1);
}
Code for DC Motor :
// Header files
#ifndef DCMOTOR_H_
#define DCMOTOR_H_
#define F_CPU 16000000UL
#include <avr/io.h>
#include <util/delay.h>
void initDCMotor();
void setMotorSpeed(int bladeMotorSpeed);
void rotateMotor();
void stopMotor();
#endif /* DCMOTOR_H_ */

## Slide 89
3. Inductive Proximity Sensor
1(Brown) - Positive(+)
2(Blue) - Negative(-)/ Ground
3(Black) - Output Signal
Datasheet:
https://realpars.com/wp-content/uploads/2020/07/Inductive-sensor-NBB1.5-5GM25-E2-V3-PEPPERL%2BFUCHS.pdf
1
2
3

## Slide 90
Internal structure:
Maximum current: 200mA
Maximum voltage: 30 VDC
Output type : PNP
Temperature : -25 ... 70 °C (-13 ... 158 °F)
Specifications:

## Slide 91
PNP Type Structure
NPN Type Structure

## Slide 92
Working Principle

## Slide 94
For Metal Pipe
For PVC Pipe

## Slide 95
Code for Inductive Proximity Sensor :
#define F_CPU 16000000UL
#include <avr/io.h>
int main()
{
DDRA=(1<<PA0);
int isMetal;
while (1)
{
if (PINB & 1 << PB5){ // Change DC motor speed
// metal
isMetal = 1; //sendData(HIGH_SPEED);
}else{
// PVC
isMetal = 0;
//sendData(LOW_SPEED);
}
//for demonstration only
if(isMetal){
PORTA |=(1<<PA0);
}else{
PORTA &=~(1<<PA0);
}
}
}

## Slide 96
PCB Design for all responsible components:

## Slide 97
Member 5- K.M. Tharangana (204215A)
Responsible Components :
LCD Display
Ultrasonic Sensor(measuring process)
Stepper motor(clutch 3)

## Slide 98
16x2 LCD Display
Guide the user to enter the needed length and quantity of pipe and display them

## Slide 99
Pin Description
Pin number | Pin | Function
1 | VSS | Ground pin
2 | VDD | 5v power supply
3 | VEE | Adjust the contrast of display. Potentiometer / variable resistor is connected and by changing the resistance we can adjust the contrast. (lower the voltage higher the contrast.)
15 | LED A | Positive supply for backlight
16 | LED K | Negative supply for backlight
Power:
Backlight:

## Slide 100
Pin number | Pin | Function
4 | RS | Register select pin. RS=0, data on pins considered as commands RS=1, data on pins considered as data to display
5 | R/W | Read/Write pin. R/W=0, write data to LCD R/W=1, Read data from LCD
6 | E | Enable pin. Used to latch the data on the pins by going high to low.
Registers:
7-10 | DB0-DB3 | Used for data transferring –lower nibble(not used in four bit mode)
11-14 | DB4-DB7 | Used for data transferring –upper nibble DB7 busy flag – if this pin is high, it means current instruction is being processed and next instruction can’t be accepted.
Data pins:

## Slide 101
Specifications
Current range: 1.5 – 2.5 mA
Voltage range: 4.8 - 5.3 V DC
Operating temperature: 0-50 C
Datasheet: https://components101.com/displays/16x2-lcd-pinout-datasheet

## Slide 102
Internal structure
16 columns and 2 rows
32 characters can be displayed at once
DDRAM (Display Data RAM ) stores the address for each position
5 x 8 dots for displaying each character
CGROM(Character Generator) has 204 defined patterns
By writing data to CGRAM user can define characters(custom characters)

## Slide 103
8-bit mode vs 4-bit mode
8-bit mode | 4-bit mode
Data and commands are sending through DB0-DB7 pins One pulse signal is required to display a single character. Thus, faster | uses only four data line DB4-DB7  save pins Since two pulse are needed, latency time is high. Do it slower
However, this speed difference is not significant as LCDs are slow speed devices. Due to this reason, we can choose 4-bit mode over 8-mode to interface LCD.

## Slide 104
Schematic Diagram :

## Slide 105
Extracted instruction codes(from datasheet) for programming
RS + RW + DB7-DB0 | Hexa decimal (0x) | Function
00 0011 0011 | 33 | Function set to 8-bit mode
00 0010 1000 | 28 | 2 lines, 5 x 8 matrix in 4-bit mode
00 0000 0001 | 01 | Clear display screen
00 1000 0000 | 80 | Cursor at home position
00 0000 1100 | 0e | Display on cursor on
00 0011 0010 | 32 | Function set to 8-bit mode again
00 1100 0000 | c0 | Go to 2nd line
11 xxxx xxxx | - | Read data

## Slide 106
Test code for LCD :
#define F_CPU 16000000UL
#include <avr/io.h>
#include <util/delay.h>
#define LCD PORTB
#define EN PD7
#define RW PC6
#define RS PC5
void lcdcmd(unsigned char cmd)
{
PORTC&=~(1<<RS);
PORTC&=~(1<<RW);
LCD=cmd & 0xF0;
PORTD|=(1<<EN);
_delay_ms(20);
PORTD&=~(1<<EN);
LCD=cmd<<4;
PORTD|=(1<<EN);
_delay_ms(20);
PORTD&=~(1<<EN);
}
void lcd_print(char *str)
{
unsigned char i=0;
while(str[i]!=0)
{
lcddata(str[i]);
i++;
}
void lcddata(unsigned char data)
{
PORTC|=(1<<RS);
PORTC&=~(1<<RW);
LCD=data & 0xF0;
PORTD|=(1<<EN);
_delay_ms(20);
PORTD&=~(1<<EN);
LCD=data << 4;
PORTD|=(1<<EN);
_delay_ms(20);
PORTD&=~(1<<EN);
}
void lcd_init()
{
DDRC=0xFF;
DDRD=0xFF;
PORTD&=~(1<<EN);
lcdcmd(0x33);
lcdcmd(0x32);
lcdcmd(0x28);
lcdcmd(0x0E);
lcdcmd(0x01);
_delay_ms(20);
}
int main(void)
{
//DDRA=0x0F;
lcd_init();
lcd_print(" HELLO USER ");
_delay_ms(100);
label1:
lcdcmd(0x01);
lcdcmd(0x0E);
delay_ms(100);
lcd_print("ENTER LENGTH");
lcdcmd(0xC0);
//some keypad commands
label2:
lcdcmd(0x01);
lcdcmd(0x0E);
_delay_ms(100);
lcd_print("ENTER QUANTITY :");
_delay_ms(100);
lcdcmd(0xC0);
}
Notes: RS + RW + DB7-DB0
Hexa decimal (0x)
Function
00 0011 0011
33
Function set to 8-bit mode
00 0010 1000
28
2 lines, 5 x 8 matrix in 4-bit mode
00 0000 0001
01
Clear display screen
00 1000 0000
80
Cursor at home position
00 0000 1100
0e
Display on cursor on
00 0011 0010
32
Function set to 8-bit mode again
00 1100 0000
c0
Go to 2nd line
11 xxxx xxxx
-
Read data

## Slide 107
2. Ultra-sonic Sensor(HC-SR04)
Measuring the length of the pipe by taking the distance till clutch 1

## Slide 108
Pin Description
Pin number | Pin | Function
1 | VCC | 5v supply
2 | Trigger | Trigger input of sensor, microcontroller applies 10micro second trigger pulse to this pin
3 | Echo | Echo output of the sensor, microcontroller read this pin to detect distance to object.
4 | Ground | Ground pin
Specifications
Working voltage: 5 V DC
Working current: 15mA
Distance range: 2-400 cm
Measuring angle: 15 degree
Trigger input pulse: 10 micro-seconds
Datasheet: https://www.mouser.in/datasheet/2/813/HCSR04-2307007.pdf
1 2 3 4

## Slide 109
Working principle
Time which echo pin remain high is captured.

## Slide 110
Image source- electronicwings .com

## Slide 111
Schematic Diagram :

## Slide 112
Building the code – counting distance
Speed = distance/ time
Distance= speed x time
(speed of sound wave is 343 meters per second at standard temperature and pressure, approx.-340)
Distance to object= 340 x time /2 (since wave is going back and forth)
= 170 x time meters
1/distance = 1/ 170 x time
1/distance =1000,000/170 x 100 x time centimeters
1/distance =58.8/time
Distance = time/58

## Slide 113
Building the code – interrupt routine(INT0/PD2)
INT0 can be level triggered or edge triggered
GICR register(General Interrupt Control Register)
0: Disable external interrupt 1: Enable external interrupt
MCUCR(MCU Control Register )
define a level trigger or edge trigger on external INT0 and INT1 pins
Image source- electronicwings .com

## Slide 114
Code for Ultrasonic sensor :
#define F_CPU 16000000UL
#include <avr/io.h>
#include <avr/interrupt.h>
#include <util/delay.h>
#include <string.h>
#include <stdlib.h>
#include "ultrasonic.h"
#include "LCD.h"
int main(void)
{
LCD_Init();
DDRD = 0b11111011;
_delay_ms(50);
initUltrasonic();
static int16_t count_a = 0;
char show_a[16];
sei();
while(1)
{
count_a =getUltrasonic_1_distance();
LCD_String_xy(0, 0, "Ultrasonic");
itoa(count_a,show_a,10);
LCD_String_xy(1, 0, "Distance= ");
LCD_String_xy(1, 10, show_a);
LCD_String_xy(1, 13, "cm");
_delay_ms(200);
}
}
#include "ultrasonic.h"
static volatile int pulse = 0; // interger to access all though the program
static volatile int i = 0;
int timerOverFlow=0;
static volatile int ult_count=NULL;
void initUltrasonic(){
GICR |= (1<<INT0); //enabling interupt 0
//General Interrupt Control Register
MCUCR|= (1<<ISC00); //setting interrupt triggering logic change
// MCU control Register
TIMSK|=(1<<TOIE0);
TCCR0 = 0;
}
int getUltrasonic_1_distance(){
int pulse;
PORTD |= (1<<PIND7);
_delay_us(15); //triggering the sensor for 15usec
PORTD &= (~(1<<PIND7));
while(ult_count==NULL);
pulse=ult_count;
ult_count=NULL;
return (pulse/58)+1;
}
ISR(INT0_vect) //interrupt service routine when there is a change in logic level
{
if (i==1)//when logic from HIGH to LOW
{
TCCR0=0; //disabling counter
ult_count=TCNT0+timerOverFlow;//count memory is updated to intege
TCNT0=0;//resetting the counter memory
i=0;
}
if (i==0)//when logic change from LOW to HIGH
{
TCCR0|=(1<<CS10);//enabling counter
i=1;
}
timerOverFlow=0;
}
ISR(TIMER0_OVF_vect)
{
timerOverFlow+=256;
}

## Slide 115
#ifndef ULTRASONIC_H_
#define ULTRASONIC_H_
#include <avr/io.h>
#include <avr/interrupt.h>
#include <util/delay.h>
#include <stdlib.h>
void initUltrasonic();
int getUltrasonic_1_distance();
#endif /* ULTRASONIC_H_ */

## Slide 116
3. Stepper Motor
Used for clutch 3 of the machine

## Slide 117: Usage : Tightening Process
After detecting and identifying the pipe, clutches will automatically move in and the pipe will be tightened.
There are four clutches which are used in the tightening process.
Two Ultra-sonic sensors are placed in both 1&2 clutches to identify the distance to the pipe by each side.

## Slide 118: Technique for Tightening Process
Inside look of the clutch
Screw Rod

## Slide 119
Internal structure:
Specifications:
Maximum current: 1.5A-1.7A
Maximum voltage: 12 VDC
Step Angle : 1.8 degree
Data sheet: https://www.omc-stepperonline.com/nema-17-stepper-motor-datasheet/nema-17-unipolar-1-8deg-15-8ncm-22-4oz-in-0-31a-12v-42x42x33mm-6-wires.html
200 Steps per revolution, 1.8 degrees
No. of Phases: 4
Unipolar

## Slide 120
Working Principle
A
B
C
D

## Slide 121
Schematic Diagram :

## Slide 122
code for Stepper Motor :
#define F_CPU 16000000UL
#include <avr/io.h>
#include "stepper.h"
int main(void){
initSteppers();
rotateStepper_3(1,1);
}
//stepper.h headerfile
#ifndef STEPPER_H_
#define STEPPER_H_
#define F_CPU 16000000UL
#include <avr/io.h>
#include <avr/interrupt.h>
#include <util/delay.h>
void initSteppers();
void rotateStepper_3(int direction, float distance);
#endif /* STEPPER_H_ */
else
{
/* Rotate Counterclockwise */
for (int i = 0; i < distance; i++)
{
PORTC = 0x03;
_delay_ms(period);
PORTC = 0x09;
_delay_ms(period);
PORTC = 0x0c;
_delay_ms(period);
PORTC = 0x06;
_delay_ms(period);
PORTC = 0x03;
_delay_ms(period);
}
_delay_ms(10);
}
}
#include "stepper.h"
void initSteppers(){
DDRA = 0xFF;
DDRC = 0xFF;
}
void rotateStepper_3(int direction, float distance){
// Counterclockwise-0
// 1 distance unit = 1 rotating
int period;
period = 100;
if (direction == 1)
{
/* Rotate clockwise */
for(int i=0;i<distance;i++)
{
PORTC = 0x03;
_delay_ms(period);
PORTC = 0x06;
_delay_ms(period);
PORTC = 0x0c;
_delay_ms(period);
PORTC = 0x09;
_delay_ms(period);
PORTC = 0x03;
_delay_ms(period);
}
_delay_ms(10);
}

## Slide 123
PCB Design for all responsible components:

## Slide 124
Stepper Motor Driver : ULN2003
Input pins can be triggered by +5V
All seven Output pins can be connected to gather to drive loads up to 3.5A.
Data sheet: https://datasheetspdf.com/pdf-file/956150/UTC/ULN2003/1

## Slide 125
DC Motor Driver: L293D
Maximum Peak motor current: 1.2A
Maximum Continuous Motor Current: 600mA
Supply Voltage to Vcc1(vss): 4.5V to 7V
Data sheet: https://datasheetspdf.com/pdf-file/69631/STMicroelectronics/L293D/1

## Slide 126: References
https://www.electronicwings.com/avr-atmega
https://tronic.lk/
https://www.youtube.com/
Grinding blade selection https://drive.google.com/file/d/1l987t_xdUDQwoZVKXyOeCLS4ZEMxx5yd/view? usp=sharing
Atmega-32 data sheet :
https://drive.google.com/file/d/1nu86kDYH1PtJV-QbK96FR9jovnH52Mws/view?usp=sharing

## Slide 127
Thank You
Questions?